## Slide 1: RSU4.1 Interface
Test and Examples
Niraj Vasant Altekar
05/23/2019

## Slide 2: Outline
RSU to MRP (BSMs/SRMs)
  RSU configuration to forward messages received over DSRC
  Receiving client on MRP
MRP to RSU (MAP/RSM/SPaT)
  Sending client on MRP
  RSU configuration to receive packets from MRP and broadcast over DSRC
RSU to Other/Other to RSU (SPaT – Signal Controller)
  RSU configuration to receive SPaT blob from the controller and broadcast over DSRC
  Signal controller configuration to forward SPaT blob to RSU
Summary and generalization for other messages

## Slide 3: Test-1: RSU to MRP
1.1. Basic Safety Message
1.2. Signal Request Message

## Slide 4: RSU to MRP – RSU Configuration (1)
4
RSU can forward the packets received over DSRC to a specified IP and port
IP and ports need to be configured for each message (distinguished by PSID)
DSRC-MESSAGE-FORWARD application hosts the configuration information
Example for BSMs is discussed.
Configuration
Status

## Slide 5: RSU to MRP – RSU Configuration (2)
5
Configure DSRC-MESSAGE-FORWARD application as follows:
  Enable the DSRC-MESSAGE-FORWARD application on the RSU:
  Add a PSID of message to be forwarded in the list of PSIDs in DSRC-MESSAGE-FORWARD application using
  Set the protocol for forwarding packets as UDP, for created PSID:
  Set the destination IP address for created PSID:
  Set the port of the listener running on the destination:
config app dsrc-message-forward psid 0x20
config app dsrc-message-forward psid 0x20 destination protocol UDP
config app dsrc-message-forward psid 0x20 destination ip 10.254.56.49
config app dsrc-message-forward psid 0x20 destination port 5000
config app dsrc-message-forward psid 0x20 destination port 5000

## Slide 6: RSU to MRP – RSU Configuration (3)
6
Configure DSRC-MESSAGE-FORWARD application (continued):
  Review the new configuration:
  If the configuration is set up as required, update the configuration to bring it into effect:
  To check the status of received (Rx) and forwarded (Tx) packets, type:
  Similar process can be followed for forwarding SRMs or any other message (again, distinguished by PSID).
config app dsrc-message-forward review
config app dsrc-message-forward updateconf
show system rsu-stats dsrc-message-forward

## Slide 7: Test-2: MRP to RSU
1.1. MAP message
1.2. Roadside Safety Message
1.3. Signal Status Message

## Slide 8: MRP to RSU– RSU Configuration (1)
8
A stream of messages can be streamed to the RSU (port 1516) from an MRP, to forward it over DSRC.
Messages need to be formatted as specified in RSU-4.1 specs.
IMMEDIATE-FORWARD application on the RSU needs to be configured to listen to the stream of messages.
Example for MAP is discussed.

## Slide 9: MRP to RSU– RSU Configuration (2)
9
Configure IMMEDIATE-FORWARD application as follows:
  Enable the IMMEDIATE-FORWARD application:
  Add a PSID of the message that will be streamed by an MRP:
  Enable listening for this PSID:
  Configure message type (i.e. DSRC-Message-ID)
  Configure Tx mode (0=Continuous, 1=Alternating)
config app immediate-forward enable
config app immediate-forward psid 0x8002
config app immediate-forward psid 0x8002 enable
config app immediate-forward psid 0x8002 dsrc-message-id 12
config app immediate-forward psid 0x8002 tx-mode 0

## Slide 10: MRP to RSU– RSU Configuration (3)
10
Configure IMMEDIATE-FORWARD application (continued):
  Configure tx-channel (172..184 – even channels):
  Review the new configuration:
  If the configuration is set up as required, update the configuration to bring it into effect:
  To check the received and forwarded packages, type:
  If required, listener port of the RSU can be changed by (not recommended):
config app immediate-forward psid 0x8002 tx-channel 172
config app immediate-forward review
config app immediate-forward updateconf
show system rsu-stats immediate-forward
show system rsu-stats immediate-forward listenerport <desired port number>